## Slide 1
Miner
Safety Helmet
GROUP NO: 28
IN 1901 - Microcontroller Based Application Development Project

## Slide 2
Group members
T. A. S. I. Jayalath
214086K
A. M. C. I. Athapaththu
214023R
A. S. F. Sahla
214177P
A. D. R. V. Abeysiri
214007X
W. A. T. M. Thilakarathna
214211R

## Slide 3
Introduction
This Project creates a special helmet for miners' safety.
The helmet has sensors to detect dangerous gases and temperatures.
It enables communication using audio transmission
The goal is to make mining safer and protect miners.
The helmet helps miners avoid hazards like harmful gases, extreme temperatures.
The project improves safety and prevents accidents in mining.
The helmet gives real-time data to help miners stay safe.
Overall, the project makes mining a safer job for miners.

## Slide 4
Problem in brief
  Mining is a dangerous job with many risks and injuries.
  Miners urgently need a safer helmet with advanced features.
  There are harmful gases for human inside Mines.
  They don’t have the ability to detect those gases.
  They cannot communicate with others when go inside.
?

## Slide 5
Block diagram
MQ4(methane) sensor
MQ7(CO) sensor
Temperature sensor
Mic
NRF24L01
(transmitter)
Input
Process
Output
NRF24L01
(receiver)
LED
Speaker
Lcd display
Push button
Convert methane, CO, temperature values analog to digital and make them to transfer
Convert voice signal analog to digital and transfer
Display received data and play received voice signal
Control send and receive voice signal
Show sensor values
Play received voice signal
Indicate voice signal come
Receive sending data
Transmit data
Inform voice transmit
Measure the sensor value
Generate voice signal
Measure the sensor value
Measure the sensor value

## Slide 6
Aim
Design a miner's safety helmet that can identify bad conditions and enables two-way audio transmission.
Objectives
Detecting harmful gases and temperature.
Enable real-time communication among miners using audio transmission features.
Provide an LCD display for monitoring and analyzing sensor data.
Improve miner safety and work efficiency through the advanced features of the safety helmet.

## Slide 7
Proposed solution
  Advanced sensors detect methane, CO concentrations (MQ4, MQ7).
  DHT22 sensors measure temperature in the mine.
  Wireless transmission enables real-time monitoring, analysis.
  Wearable helmet design provides convenience, constant monitoring.
  NRF24 module enables audio transmission between miners.
  LCD display shows real-time data on gas, temperature.

## Slide 8
3D design
Receiver station
Helmet

## Slide 9
Resource required
Software
  Arduino IDE - codes
  Blender – 3D design
  EasyEDA – PCB layout
Hardware
  MQ4 sensor
  MQ7 sensor
  DHT22 sensor
  NRF24L01
  Arduino nano
  Arduino uno
  mics
  16x4 display
  Speakers

## Slide 10: Cost estimate
Item | Quantity | Unit price(Rs) | Price(Rs)
Arduino nano | 1 | 2530 | 2530
Arduino uno | 1 | 1500 | 1500
NRF 24L01 | 3 | 860 | 2580
MQ4 sensor | 1 | 540 | 540
MQ7 sensor | 1 | 550 | 550
DHT22 temperature sensor | 1 | 800 | 800
16*4 Lcd display | 1 | 1200 | 1200
NRF 24L01 Base module | 3 | 275 | 825
I2C Adapter Board | 1 | 250 | 250
PAM8403 stereo audio amplifier | 2 | 130 | 260
8 Ohm 0.5W Speaker | 2 | 100 | 200
Condenser mic | 2 | 40 | 80
LM2596 buck converter | 1 | 320 | 640
5V SMPC power adapter | 2 | 550 | 1100
3.7V 18650 battery | 2 | 1020 | 2040
Other |  |  | 5000
Total |  |  | 19875

## Slide 11
Individual contribution

## Slide 12
214086K
T. A. S. I. Jayalath
NRF24L01 basics
Transmitter and part of NRF24L01
Compilation of code
Responsibilities

## Slide 13
NRF24L01
Specification
  2.4GHz RF transceiver Module
  Operating Voltage: 3.3V
  Communication Protocol: SPI
  Baud Rate: 250 kbps - 2 Mbps.
  Channels: 126
  Low-cost wireless solution
Datasheet

## Slide 14
Base module for NRF24L01
Specification
  Compatible 8-pin NRF24L01 Series RF Module
  Input Voltage: 5V ~ 15V
  Output Voltage: 3.3V
  Provides power stabilization

## Slide 15
Schematic diagram of NRF24L01 transmitter

## Slide 16
Transmitter code
#include <RF24.h>
#include <SPI.h>
#include <nRF24L01.h>
RF24 radio(7, 8);
// Set radio up using pins 7 (CE) 8 (CS)
// Struct to hold the sensor values
struct SensorData {
float temperature;
float co_ppm;
float methane_ppm;
};
void setup() {
radio.begin();
radio.openWritingPipe(0xF0F0F0F0E1LL);
// Address to send to (6-byte alphanumeric)
}
void sendMessage() {
// Read the temperature data from the DHT22 sensor
float temperature = dht.readTemperature();
// Read the CO data from the MQ7 CO sensor
float co_ppm = readCOConcentration();
// Read the CO data from the MQ7 CO sensor
float methane_ppm = mq4Value();
// Create a struct to hold the temperature and CO values
SensorData data;
data.temperature = temperature;
data.co_ppm = co_ppm;
data.methne_ppm = methaneppm;
// Send the temperature and CO data over the radio module
radio.write(&data, sizeof(data));
}
void loop(){
sendMessage();
delay(1000);
}

## Slide 17
214023R
A. M. C. I. Athapaththu
Receiver and repeater part of NRF24L01
Lcd display
I2C module for display
Responsibilities

## Slide 18
Schematic diagram of NRF24L01 receiver

## Slide 19
Receiver code
#include <SPI.h>
#include <nRF24L01.h>
#include <RF24.h>
// Setup the radio module
RF24 radio(7, 8); // CE, CSN
// Define the struct to hold temperature and CO values
struct SensorData {
float temperature;
float CO_ppm;
float other_value;
};
SensorData sensorData; // Create an instance of the struct
void setup() {
Serial.begin(9600);
// Setup the radio module
radio.begin();
radio.openReadingPipe(1, 0xF0F0F0F0D2LL);
radio.startListening();
}
void loop() {
if (radio.available()) {
radio.read(&sensorData, sizeof(sensorData));
// Print the received data
Serial.print("Temperature: ");
Serial.print(sensorData.temperature);
Serial.print(" degC\tCO: ");
Serial.print(sensorData.CO_ppm);
Serial.println("Metane PPM ");
Serial.print(sensorData.other_value );
}
}

## Slide 20
Schematic diagram of NRF24L01 repeater

## Slide 21
Repeater code
#include <SPI.h>
#include <RF24.h>
RF24 radio(7, 8); // CE, CSN pins
// Define the struct to hold temperature and CO values
struct SensorData {
float temperature;
float CO_ppm;
float other_value;
};
SensorData sensorData;
void setup() {
radio.begin();
radio.openReadingPipe(1, 0xF0F0F0F0E1LL);
// Address to receive from (6-byte alphanumeric)
radio.openWritingPipe(0xF0F0F0F0D2LL);
// Address to transmit to (6-byte alphanumeric)
radio.startListening();
}
void loop() {
if (radio.available()) {
radio.read(&sensorData, sizeof(sensorData));
radio.stopListening();
radio.write(&sensorData, sizeof(sensorData));
radio.startListening();
}
}

## Slide 22
16x4 LCD Display
Specification
  Contains 16 pins
  Operate in 4bit mode or 8bit modes.
  Resolution:16 columns and 4 rows
  Total Characters: 64 (16x4)
  Used to display sensor values and mine condition
  Viewing area: 60x32.6mm
  I2C communication protocol
Datasheet

## Slide 23
I2C PCF8574T
  Reduce no of wires
  Contains PCF8574T chip
  Using I2C can adjust the display’s contrast
  Only used two pins to connect LCD to the Arduino board
  (SDA, SCL)
Specification
  Maximum voltage 7V
  Maximum current 20mA
  Operating Temperature -20° C to +70°°C
  I2C Address range - 0x20 to 0x27
  (Default =0x27,Addressable)
Datasheet
GND
VCC
SDA
SCL
Backlight Jumper

## Slide 24
Schematic diagram of I2C and Lcd display

## Slide 25
I2C lcd display code
#include <LiquidCrystal_I2C.h> //libraries for lcd display
#include <Wire.h>
LiquidCrystal_I2C lcd(0x27, 16, 4); // Set the I2C address and dimensions of the display
void setup() {
lcdsetup(); //calling lcdsetup function for setting up the lcd display
}
//lcd display function for the begining of the receiver station
void lcdsetup() {
lcd.begin(); // Initialize the LCD
lcd.backlight(); // Turn on the backlight
lcd.setCursor(0, 1); // Set the cursor to the beginning of the second line
lcd.print("____MINOR_____"); // Print a message
lcd.setCursor(-4, 2); // Set the cursor to the beginning of the third line
lcd.print("_SAFETY HELMET");
delay(1000);
lcd.clear(); //clear the display
}
//lcd display function when sensor values receiving
void lcdloop(float temp, float meth, double co) {
lcd.setCursor(0, 0); // Set the cursor to the beginning of the first line
lcd.print("MINE CONDITION");

## Slide 26
lcd.setCursor(0, 1); // Set the cursor to the beginning of the second line
lcd.print("Temp(c) :");
lcd.print(temp);
lcd.setCursor(-4, 2); // Set the cursor to the beginning of the third line
lcd.print("Methan(ppm):");
lcd.print(meth);
lcd.setCursor(-4, 3); // Set the cursor to the beginning of the fourth line
lcd.print("CO(ppm) :");
lcd.print(co);
}
//lcd display function when audio transmission
void lcdLoopAudio(){
lcd.clear(); //clear the display
lcd.setCursor(2, 0);
lcd.print("Audio->");
lcd.print(124-(millis()/1000)); //display the remaining seconds of audio transmission
lcd.print(" Sec");
lcd.setCursor(0, 1);
lcd.print("Temp(c) :");
lcd.print(tempAudio);
lcd.setCursor(-4, 2);
lcd.print("Methan(ppm):");
lcd.print(CH4Audio);
lcd.setCursor(-4, 3);
lcd.print("CO(ppm) :");
lcd.print(CoAudio);
delay(1000);
}

## Slide 27
214211R
W. A. T. M. Thilakarathna
Audio transmission part of NRF24L01
Power supply
Designing the PCB
3D design
Making the structure
Responsibilities

## Slide 28
Schematic diagram of NRF24L01 audio transmission circuit

## Slide 29
NRF24L01 audio transmission code
#include <RF24.h>
#include <SPI.h>
#include <RF24Audio.h>
RF24 radio(7,8);
// Set radio up using pins 7 (CE) 8 (CS)
RF24Audio rfAudio(radio, 1);
const int buttonPin = 2; // Replace with the actual pin number of the button
bool pressButton = false;
void setup() {
radio.begin();
rfAudio.begin();
rfAudio.setVolume(7);
}
void loop() {
// Check if the button is pressed
if (digitalRead(buttonPin) == HIGH) {
// Button is pressed, start transmitting audio
if (!pressButton) {
rfAudio.transmit();
pressButton = true;
}
} else {
// Button is not pressed, start receiving audio
if (pressButton) {
rfAudio.receive();
pressButton = false;
}
}
}

## Slide 30: PAM8403 audio amplifier
Specification
  Dual channel stereo output 3W+3W power Class D
  High amplification efficiency 85%
  Can directly drive 4Ω / 8Ω small speakers
  Good sound quality & noise suppression
  Unique without LC filter class D digital power board
  Can use computer USB power supply directly
Datasheet

## Slide 31
LM2596 buck converter
Specification
  Input voltage 3.2V ~ 40V
  Output voltage 1.25V ~ 35V
  Output current 3A (max)
  The conversion efficiency of 92% (maximum)
Datasheet

## Slide 32
TP4056
2S Lithium-ion Battery Protection Board
Specification
  Short circuit protection
  Overcharge protection
  Overcurrent protection
  Maximum Working Current: 3A
  Operating Temperature: -40 to 50°C
  Internal Resistance: Less than 45mΩ
Datasheet

## Slide 33
Schematic diagram of power supply

## Slide 34: PCB layouts
Transmitter
Receiver
Repeater

## Slide 35
214007X
A. D. R. V. Abeysiri
Arduino basics
MQ4 sensor
DHT22 temperature sensor
Responsibilities

## Slide 36
MQ4 sensor
Specification
  Circuit and heating voltage - 5V
  Load resistance - 20 k ohm
  Heater resistance - 33 ohm
  Heating consumption - less than 750mw
  Using temperature - -10℃-50℃
  Storage temperature - -20℃-70℃
  Detecting concentration - 200ppm - 10000ppm
  Sensing resistance - 10KΩ- 60KΩ
Datasheet

## Slide 37
Schematic of MQ4 sensor

## Slide 38
MQ4 code
const int MQ4Sensor = A0;
// MQ4 Sensor output connected to Arduino's A0 pin
// Calibration value
float R0 = 10.0;
// This is the resistance in the sensor in clean air at 1000ppm
float RL = 20.0;
void setup() {
Serial.begin(9600);
}
void loop() {
float sensor_volt;
float RS_gas; // Get value of RS in a GAS
float ratio; // Get ratio RS_gas/RS_air
sensor_volt = analogRead(MQ4Sensor);
sensor_volt = sensor_volt/1024*5.0;
RS_gas = ((5.0-sensor_volt)/sensor_volt)*RL;
// Calculate RS in GAS
ratio = RS_gas/R0; // ratio = RS/R0
ppm= pow(ratio,-1.85);
Serial.print("ppm= ");
Serial.println(ppm);
delay(1000);

## Slide 39
DHT22 temperature sensor
Specification
  Power supply - 3.3- 6V DC
  Operating range - -40~80Celsius
  temperature <+-0.5Celsius
Datasheet

## Slide 40
Schematic of DHT22 sensor

## Slide 41
DHT22 code
#include <DHT.h>
// Setup the DHT22 sensor
#define DHTPIN 4 // Digital pin connected to the DHT sensor
#define DHTTYPE DHT22 // DHT22 (AM2302)
DHT dht(DHTPIN, DHTTYPE);
void setup(){
// Setup the DHT22 sensor
dht.begin();
serial.begin(9600);
}
void loop(){
// Read the temperature data from the DHT22 sensor
float temperature = dht.readTemperature();
serial.print("temp= ");
serial.println(temperature);
delay(1000);
}

## Slide 42
214177P
A. S. F. Sahla
MQ7 sensor
DHT22 temperature sensor
Responsibilities

## Slide 43
MQ7 sensor
Specification
  Circuit voltage 5V
  Heating voltage high 5V
  Heating voltage low 1.4V
  Load resistance - can adjust
  Heating resistance - 33 ohm
  Using temperature - -20℃-50℃
  Storage temperature - -20℃-50℃
  Detecting range - 20ppm - 2000ppm
Datasheet

## Slide 44
Schematic of MQ7 sensor

## Slide 45
MQ7 code
int gas_sensor = A0; // Sensor pin
float m = -0.6527; // Slope
float b = 1.30; // Y-Intercept
float R0 = 21.91;
// Sensor Resistance in fresh air from previous code
void setup() {
Serial.begin(9600); // Baud rate
pinMode(gas_sensor, INPUT); // Set gas sensor as input
}
void loop() {
float ppm = readCOConcentration();
// Read CO concentration value from the sensor
Serial.print("CO Concentration (ppm) = ");
Serial.println(ppm);
delay(2000);
}
float readCOConcentration() {
float sensor_volt;
// Define a variable for sensor voltage
float RS_gas;
// Define a variable for sensor resistance
float ratio; // Define variable for ratio
int sensorValue = analogRead(gas_sensor);
// Read analog values of the sensor
Serial.print("GAS SENSOR RAW VALUE = ");
Serial.println(sensorValue);
sensor_volt = sensorValue * (5.0 / 1023.0);
// Convert analog values to voltage
Serial.print("Sensor value in volts = ");
Serial.println(sensor_volt);
RS_gas = ((5.0 * 10.0) / sensor_volt) - 10.0;
// Get value of RS in a gas
Serial.print("Rs value = ");
Serial.println(RS_gas);
ratio = RS_gas / R0; // Get ratio RS_gas/RS_air
Serial.print("Ratio = ");
Serial.println(ratio);
double ppm_log = (log10(ratio) - b) / m;
// Get ppm value in linear scale according to the ratio
double ppm = pow(10, ppm_log);
// Convert ppm value to log scale
Serial.print("CO Concentration (ppm) = ");
Serial.println(ppm);
return ppm;
}

## Slide 46
Testing video

## Slide 47
Schematic of transmitter

## Slide 48
Schematic of receiver

## Slide 49
Schematic of repeater

## Slide 50: Q & A

## Slide 51
THANK YOU!